## Slide 1
MultiRabber –automation system

## Slide 2
MultiRabber key things
- Successful authentication with server is required until functions are activated in MultiRabbers
- MultiRabber is application which executes HTTP DL, HTTP UL, SMS, WEB VIEW and CALL automations tests
- HTTP DL, HTTP UL, SMS and WEB VIEW-tests can be run parallel
- App do not work on background. It have to be open and visible in UE screen all the time
- Limitations for CALL test:
- Automatic answering: connect HF and select “AutoAnswer” from android system settings
- Not possible to terminate call
- When call is terminated then new call is done after 15 sec, if STOP has not been received
- MultiRabber sends results to server when it receives STOP -command with parameter “Send results to server”
MultiRabber_controller key things
Successful authentication with server is required until functions are activated in MultiRabber_controller
MultiRabber_controller is application which is used to start tests on MultiRabbers
Control messages between Controller and MultiRabber goes to top of SMS
Tests can be started multiple MultiRabbers at the same time
App do not work on background. It have to be open and visible in UE screen all the time
User can define 3 different Test Sequencies
Trigger –function can be used to start tests automatically e.g when new SW Build is ready
STOP –command can have 2 parameters
  “Clear results from MultiRabbers” (if not checked then MultiRabber is adding results cumulatively)
  “Send results to server” (If checked then MultiRabber sends results to server)

## Slide 3
Sequence checked
Select tests for SEQ 1,2 and 3
Timeout 5sec
START TESTS click
Start SEQ timer
Start SEQ 1/2/3 tests
SEQ timer expires
1min fixed timer
STOP tests
Send test command to UE
NO
YES
Presetup:
- DL, UL, SMS, WEB and CALL test parameters are defined (read NOTE for the CALL test)
- Test UE numbers are defined for controller
Test sequence timer is defined (e.g 60 min)
NOTE: Call test can be only alone. Currently not possible to stop call.
MultiRabber_Controller: Test Sequence -functionality
TRIGGER STOP button stops ongoing TRIGGER and SEQ functions from Controller. It does not STOP
Tests from MultiRabbers ! STOP tests manually from MultiRabbers or use Controller to STOP tests.
More test UE numbers defined ?

## Slide 4
TRIGGER Checked
Disable START TESTS button
Trigger file polling 30sec timer
Start testrun timer
Is SEQ checked ?
TRIGGER START click
Start Tests
NO
Start SEQ timer
Start SEQ 1/2/3 tests
SEQ timer expires
1min fixed timer
YES
STOP tests
Trigger file found
Yes
No
Testrun timer expires
STOP all ongoing tests
5min timeout
Presetup:
- DL, UL, SMS, WEB and CALL test parameters are defined (read NOTE for the CALL test)
- Test UE numbers are defined for controller
- Test sequence is defined, if needed
- Test run timer is defined (e.g 240 min)
NOTE: Call test can be only alone. Currently not possible to stop call.
MultiRabber_Controller: Trigger functionality with Test Sequence -function
TRIGGER STOP button stops ongoing TRIGGER and SEQ functions from Controller. It does not STOP
Tests from MultiRabbers ! STOP tests manually from MultiRabbers or use Controller to STOP tests.